## Slide 1: Using ESAP-Calibrate and ESAP-SaltMapper
How to create effective calibrations of EMI readings to other soil characteristics

## Slide 2: Open ESAP-Calibrate from the main ESAP menu

## Slide 3: Import Survey Data File

## Slide 4: Import .svy file generated from ESAP-RSSD

## Slide 5: Create New Profile Data File

## Slide 6: Input Lab Data as .csv in correct format. Under “Data Input File Format” click “Generic”

## Slide 7: Fill in boxes with appropriate values and press “OK”

## Slide 8: At the main menu, go to the Regression Modelling module

## Slide 9: At the menu under “File” go to “Edit of Validate Profile Data”

## Slide 10: Compute summary statistics, then save your results

## Slide 11: At the main menu, go to the Regression Modelling module

## Slide 12: Select Response Variable and Merge Data. Accept Results.

## Slide 13: “Model”  “Identify model parameters”  “Auto-Select an appropriate model”  “Analyze all possible models”  Invoke

## Slide 14: View Results (optional) to obtain PRESS score rankings, and then accept selection

## Slide 15: “Model”  “Estimate calibration equation”  Check both boxes “Estimate”

## Slide 16: “Model”  “Advanced modeling options”  “View model summary statistics”  “Specify Output File Name”  “Finished”
THIS FILE HAS THE REGRESSION EQUATION COEFFICIENTS FOR EACH DEPTH AND AVERAGE

## Slide 17: Optional: View prediction plots for accuracy

## Slide 18: “Predict”  “Calculate field summary statistics”  Specify Soil Variable  Specify Cut-off values  “Calculate Statistics”

## Slide 19: Specify Output File Name  Save File  Finished

## Slide 20: “Predict”  “Manipulate prediction data”  “Save output Predictions”  “Specify output file name”  “Finished”

## Slide 21: Calibration is Now Complete!
Additional options from here:
  Yield loss predictions
  Mean-Shift Tests to see if salt content in a field has changed from one EM38 survey to another
  Net-Flux tests to see if salt content in a single sample site location has changed via additional soil samples
To view calibration equations directly:
  Find the project folder in the file explorer and open the file created in slide 16. An example of an equation is shown

## Slide 22: The ESAP-Calibrate Predictions are Now Ready for Use for ESAP-SaltMapper

## Slide 23: Select ESAP-SaltMapper from the “Programs” and “Analysis Software” menus.

## Slide 24: Select Specify/Input File Info from the “File” menu.

## Slide 25: Specify the project and input file location

## Slide 26: Select 2-D Raster Image Map from “Graphics” menu.

## Slide 27: Initialize the Raster Window, then Show the Grid/Survey Sites

## Slide 28: Clip the grid to the appropriate field shape. Yellow indicates clipped area.
Press, “Done”

## Slide 29: Set the Kernel Size Dense survey grid (6%) Sparse survey grid (10%+)
Press “Done”
Press “Perform Interpolation”

## Slide 30: Accept Interpolation Grid After Checking Boundaries

## Slide 31: Select Specify Map Variable from the “Plot” menu.

## Slide 32: Customize Variable, Map Features, and Map Appearance. Sample sites may also be overlaid.
Press “OK”

## Slide 33: Select Create Map from the “Plot” menu

## Slide 34: You can now view your salinity map. Select Enlarge Map for Output from the “Plot” menu to view or print your map.

## Slide 35: Final Product!

## Slide 36: Questions